XMC1303 pin assignment Tongsheng Controller
Pin	Port	Funktion	Cable color/connector
1	2.4	U Battery 1,99V @ 34,6 Vbat
2	2.5	Analog input J7 left, J7 right = 5V (not used)
3	2.6	Anlalog input over 2k2 to FB Pin XL7005A (Voltage measurement)
4	2.7	Ca. 2,2V (unknown origin)
5	2.8	Current Total ADC
6	2.9	Current Phase U ADC
7	2.10	Current Phase V ADC
8	2.11	Current Phase W ADC
9	VSS
10	VDD
11	1.5	Light switching output
12	1.4	high
13	1.3	PWM out Torque sensor, pulse length 2.5µs high, distance 20µs
14	1.2	Hallsensor 3	Hall cable blue
15	1.1	Hallsensor 2	Hall cable yellow
16	1.0	Hallsensor 1	Hall cable green
17	0.0	PWM High Phase U	Motor cable green
18	0.1	PWM Low Phase U
19	0.2	PWM High Phase V	Motor cable blue
20	0.3	PWM Low Phase V
21	0.4	Speed Signal	Sensor cable white
22	0.5	PAS 1 Signal	PAS cable blue
23	0.6	RX Display communication	Display cable orange
24	0.7	TX Display communication	Display cable brown
25	VSSP
26	VDDP
27	0.8	PWM High Phase W	Motor cable yellow
28	0.9	PWM Low Phase W
29	0.10
30	0.11
31	0.12
32	0.13	PAS 2 Signal	PAS cable yellow
33	0.14	SWD Debug Pin	Sensor cable purple
34	0.15	SWCLK Debug Pin	Sensor cable black
35	2.0	Serial signal on unused pad 1
36	2.1	Input from unused pad 2
37	2.2	Analog value torque sensor
38	2.3	Analogsignal 2,5V
		Lichtausgang +6V	Sensor cable green
		U Mos Driver and torque sensor 12,7V
		GND	Sensor cable orange
		+5V	Sensor cable brown
		GND	Display cable black
		VBatt	Display cable green
		VBatt Motor Ein Spannung kommt von Display	Display cable white
		Vermutlich Brake Sensor	Display cable purple

Torque sensor supplies negative pulse (approx.5µs) with level that is torque dependent.
Inductance L = 76µH 36V Motor, 135µH 48V Motor.